## Slide 1: CONTROLLER TEMPERATURE OUT OF SPEC INVESTIGATION
NOC: INC-11460

## Slide 2
Issue Definition
What We Know
Further Observations
Recommendations

## Slide 3: Issue Definition
Error 069 takes a number of KPs out of service at varying regularity when the controller temperature exceeds 50°c depending on the daily weather conditions.
The KPs with most frequent occurrences have been established to be mounted in locations where they are exposed to direct sunlight at certain times during the day.
The time period this is likely to be experienced is between 11.00a.m and 3.00p.m

## Slide 4: What We Know
max controller temperature | 66°c
median of unique max controller temperatures | 55°c
mode of max controller temperatures | 50°c
Count of KPs with at least 1 out of service case | 160
All values below refer data between 1/1/2020 and 4/1/2020
The actual spike above threshold happens during a dispense in the period that the sunlight is striking the KP facade (attributed to the temperature of the inductor for the dispense actuators)
Bidii which is in the open and suffers the highest values (>60°c) does not have its out of service during dispenses as the rise due to sunlight is always very high

## Slide 5: Further Observations
max tablet CPU temperature | 120°c
mode of max tablet temperatures | 83°c
Count of KPs with tablet temp above 83°c | 106
The tablet CPU temperature is also affected by the exposure to sun rays
INC-14441 on Fresh Service reports the tablet screen of KP-0432 (of max tablet CPU temperature = 100°c) to be going off and on mid dispense while also being unresponsive to touch

## Slide 6: Recommendations
The Controller Temperature higher threshold (TCH) be set to 58°C
The KP at Shell Bidii be covered in a way that protects it from prolonged exposure to the sun. This applies to KPs that can’t be relocated too.
KPs that can be relocated within the agent shop to be relocated to protect the tablet from registering temperatures above 100°C